## Slide 1: Slot 01: Introduction to PFC
Languages and C Compilers
First Program in C

## Slide 2: Objectives
This chapter supplies basic concepts in computer programming. After studying this chapter, you should be able to:
Define concepts: computer program, computer software, Information, data, fundamental Data Units, data address
Explain how to make a good software?
Understand steps to develop a software?
Explain ways to represent data
Answer why C is the first language selected
Understand how a C program can be translated and execute
Discuss about notable features of C
Understand a C program structure

## Slide 3: Contents
Definitions: computer program, computer software
How to make a good software?
Steps to develop a software?
Computer hardware.
Information, Data, Fundamental Data Units
Data Representation
Addressing Information
Program Instructions
Languages
Translate and execute a program
Why C is the first language selected?
Some notable features of C
Structure of a simple C Program.

## Slide 4: 1.1- Definitions
Computer program:
  A simulation of solution.
  Is a set of instructions that computer hardware will execute
  Increase performance of standard workflow (dòng công việc)
Computer software:
  - A set of related programs
P1
P2
P3
Pn
Pn

## Slide 5: 1.2- How to make a good software?
Issues for a program/software:
  Usability
    robust and user-friendly interfaces
  Correctness
    comprehensive testing
  Maintainability
    Understandability
      structured programming
      internal documentation
    Modifiability
      standards compliance
  Portability
    standards compliance

## Slide 6: 1.3- Steps to develop a software
  Requirements
  Analysis
  Design
  Coding
  Testing
  Deploying
  Maintenance

## Slide 7: 1.4- Computer Hardware - Review
Bus | Used to
Address bus | Determine the IO peripherals, position of accessed memory.
Data bus | Transmit data
Control bus | Determine operation on peripherals, read peripheral ‘s states
3 bước giúp đọc 1 ô nhớ:
CPU áp đặt dữ liệu địa chỉ ô nhớ lên address bus
CPU áp đặt tín hiệu “đọc” lên control bus.
Data trong ô nhớ sẽ theo data bus về 1 thanh ghi của CPU.

## Slide 8: 1.4- Computer Hardware…
The most expensive and fastest memory - registers - is reserved for the CPU.
  CPU transfers information at less than 10 nanoseconds
  primary memory transfers information at about 60 nanoseconds
  a hard disk transfers information at about 12,000,000 nanoseconds
CPU memory is volatile - the contents of the registers are lost as soon as power is turned off.

## Slide 9: 1.4- Computer Hardware…
Primary Memory
  Primary memory holds the information accessed by the CPU.
  Primary memory is also volatile.
  The popular term for primary memory is RAM (Random Access Memory).

## Slide 10: 1.4- Computer Hardware…
Devices
  Include I/O devices such as a keyboard, a monitor and a mouse…
  Storage devices such as a floppy drive, a hard drive and a CD-ROM drive (secondary storage).
  Each device interfaces with the system buses through a device controller.

## Slide 11: 1.4- Computer Hardware…
Devices
  Include I/O devices such as a keyboard, a monitor and a mouse…
  Storage devices such as a floppy drive, a hard drive and a CD-ROM drive (secondary storage).
  Each device interfaces with the system buses through a device controller.

## Slide 12: 1.5- Information/Data
Data: specific values that describe something
Information: Meaning of data
Program information consists of instructions and data.
  How is this information stored?
  What does a program instruction look like?
  How do we make program instructions readable?

## Slide 13: 1.6- Data Units
John von Neumann selected binary (base 2) digits as the EDVAC's fundamental unit.
The vast majority of modern computers process and store information in binary digits.
We call a binary digit a bit.
One nibble consists of 4 consecutive bits.
The fundamental addressable unit of primary memory is the byte  One byte consists of 2 nibbles.
Byte |  |  |  |  |  |  | 
Nibble |  |  |  | Nibble |  |  | 
Bit | Bit | Bit | Bit | Bit | Bit | Bit | Bit
00000000 <- possibility 0 00000001 <- possibility 1 00000010 <- possibility 2 00000011 <- possibility 3 00000100 <- possibility 4 ... 00111000 <- possibility 104 ... 11111111 <- possibility 255

## Slide 14: 1.6- Data Units …
The natural unit of the CPU is a word. A word is the size of the general registers - the unit of memory within the CPU.

## Slide 15: 1.7- Data Representations
3 common number systems:
  Decimal Representation
  Hexadecimal Representation
    Base 16: 0, 1, …, 9, A, B, C, D, E, F
    Each hexadecimal digit represents 4 bits of information.
    The 0x prefix identifies the number as a hexadecimal number: 0x5C
  Octal Representation
    Base 8: 0, 1, 2, .., 7
    Set of 3 consecutive bits forms an octal digit
    The prefix 0 identifies the number as an octal number: 031

## Slide 16: Data Representations: Conversion- A review
Read by yourself

## Slide 17: Data Representations: Conversion: A review
Read by yourself

## Slide 18: Data Representations: Conversion: A review
Read by yourself

## Slide 19: Data Representations: Conversion…
Máy tính là thiết bị nhị phân nên tất cả mọi dữ liệu đều được lưu trữ dạng nhị phân.
Số quả dâu:
3
3
00110011
3
Dạng mô tả của người
Mã hóa
Giải mã sang dạng biểu diễn của người
Read by yourself

## Slide 20: Data Representations: Conversion…
Decimal | 4-bit Binary | Decimal | 8-bit Binary | Decimal | 16-bit Binary
9 | 1001 | 7 | 0000 0111 | 255 | 0000 0000 1111 1111
7 |  | 34 |  | 192 | 
2 |  | 125 |  | 188 | 
15 |  | 157 |  | 312 | 
12 |  | 162 |  | 517 | 
11 |  | 37 |  | 264 | 
6 |  | 66 |  | 543 | 
5 |  | 77 |  | 819 | 
8 |  | 88 |  | 1027 | 
13 |  | 99 |  | 2055 | 
14 |  | 109 |  | 63 | 
Fill the corresponding binary expansions of the following decimal number:
Read by and do yourself

## Slide 21: Data Representations: Conversion…
Decimal | Binary | Hexa. | Decimal | 16-bit Binary | Hexadecimal
9 | 1001 | 9 | 255 | 0000 0000 1111 1111 | 00FF
127 | 0111 1111 | 9F | 192 |  | 
125 |  |  | 188 |  | 
157 |  |  | 312 |  | 
162 |  |  | 517 |  | 
37 |  |  | 264 |  | 
66 |  |  | 543 |  | 
77 |  |  | 819 |  | 
88 |  |  | 1027 |  | 
99 |  |  | 2055 |  | 
109 |  |  | 63 |  | 
Fill the blank cells
Read by yourself

## Slide 22: Data Representations: Operations
Do yourself:
3245q + 247q
1A7Bh + 26FE7h
101101111 b
100111011 b
110110001 b
110001101b
+
Read by yourself

## Slide 23: Data Representations: Operations …
Do yourself
1101101101b - 10110111b 3654q – 337q 3AB7h – 1FAh
36Ah – 576q = ? h 64AEh – 1001101b= ? q
Read by yourself

## Slide 24: Data Representations: Operations …
Bài tập : Làm các phép tính
1011010 b* 1011b
1101000b + 2AB h + 345 q = ? h = ? q
3AFh / 1Ch =? b = ?d
3ACh – 562q = ?b = ? d
3FFA h / 327q = ?b = ? d
Read by yourself

## Slide 25: Data Representations: Operations …
Read by yourself

## Slide 26: Data Representations: Signed Integers
Dùng
bit trái (leftmost bit) để mô tả dấu:
0:positive, 1:negative
Read by yourself

## Slide 27: Data Representations: Signed Integers
Tìm biểu diễn của –35 với 1 byte
Cách làm: Ta tìm biểu diễn của +35 rồi tìm bù 2 của nó ta được biểu diễn số âm
Tìm trị của biểu diễn số nguyên có dấu 1 byte 11111100 b
Bít trái : 1  Biểu diễn số âm. Nếu ta tìm được biểu diễn dương tương ứng, tìm trị , thêm dấu trừ ta được trị kết qủa.
Bài tập
Tìm biểu diễn của số nguyên không dấu 1 byte: 251 , 163, 117
Tìm biểu diễn của số nguyên không dấu 2 byte: 551 , 160, 443
Tìm biểu diễn của số có dấu 1 byte: -51 , -163, -117, 320
Tìm trị của biễu diễn số nguyên có dấu 1 byte :
01100011 b , 10001111 b , 11001010 b , 01001100 b
Read by yourself

## Slide 28: 1.8- Addressing Information
Each byte of primary memory has a unique address, start from zero
  Kilobyte = 1024 bytes
  Kilo K= 1024 ( 210)
  Mega or M (=1024k)
  Giga or G (=1024M)
  Tera or T (=1024G)
  Peta or P (=1024T)
  Exa or E (=1024P)
Addressible Memory
  The maximum size of addressable primary memory depends upon the size of the address registers
 | MEMORY
… | …….
5 | 1010 1010
4 | 0011 1100
3 | 0101 0100
2 | 1001 0000
1 | 1100 1011
0 | 0100 0001
B: byte
b: bit

## Slide 29: 1.9- Program Instructions
Each program instruction consists of an operation and operands
The CPU performs the operation on the values stored as operands or on the values stored in the operand addresses.
Operands: Constants, registers, primary memory addresses
01001011 | 100110110110 | 011011010111
Opcode | Operand 1 | Operand 2

## Slide 30: 1.9- Program Instructions…
High-level language code
Assembly
(low-level)
code
Machine (binary)
code
compiler
assembler

## Slide 31: 1.10- Programming Languages
Programs that perform relatively simple tasks and are written in assembly language contain a large number of statements.
Machine Language  Assembly language  High-level languages,
To make our programs shorter, we use higher-level languages.

## Slide 32: 1.10- Programming Languages…
5 Generations of Programming Languages:
  (1) Machine languages.
  (2) Assembly languages.
  (3) Third-generation languages. These are languages with instructions that describe how a result is to be obtained (C, Pascal, C++, Java…).
  (4) Fourth-generation languages. These are languages with instructions that describe what is to be done without specifying how it is to be done (SQL).
  (5) Fifth-generation languages are the closest to human languages. They are used for artificial intelligence, fuzzy sets, and neural networks (Prolog, Matlab)

## Slide 33: 1.10- Programming Languages…
The higher the level, the closer to the human languages and the further from native machine languages
  Each third generation language statement ~ 5-10 machine language statements.
  Each fourth generation language ~ 30-40 machine language statements.

## Slide 34: 1.11- Translate and Execute a Program
When we code a program in a high level language, we write source code. We translate this code into machine language.
2 ways of translations:
  Interpreting: Translate and execute statements one-by-one  Interpreter
  Compiling: Translate all the program then execute all the program  Compiler
C translator is a compiler

## Slide 35: 1.12- Why C is the 1st Language?
C is one of the most popular languages in use globally
Some reasons for learning programming using the C language include:
Language | Time to Run
Assembly | 0.18 seconds
C | 2.7 seconds
Basic | 10 seconds
Comparative times for a Sieve of Eratosthenes test
  C is English-like,
  C is quite compact - has a small number of keywords,
  A large number of C programs need to be maintained,
  C is the lowest in level of the high-level languages,
  C is faster and more powerful than other high-level languages,
  The UNIX, Linux and Windows operating systems are written in C and C++.

## Slide 36: 1.13- Some Notable C Features
Comments
  /* */
  We use comments to document our programs and to enhance their readability. C compilers ignore all comments.
Whitespace
  We use whitespace to improve program readability and to display the structure of our program's logic. C compilers ignore all whitespace
Case Sensitivity
  C language is case sensitive.
  C compilers treat the character 'A' as different from the character 'a' .

## Slide 37: 1.14- Structure of a Simple C Program
Comment for program description
Declaration for library using
Entry point of C-program
Statements + comments
Exit point of C-program

## Slide 38: Structure…: C program Entry Points
Entry point: the point that a program begins.
Entry points of C-programs:
[int] main( int argCount, char* args[])
{ <statements>
[ return number; ]
}
Demo.
In the module H (Files)
Common form
[int] main( [void] )
{ <statements>
[ return number; ]
}

## Slide 39: Summary
Definitions: computer program, computer software
How to make a good software?
Steps to develop a software?
Computer hardware.
Information, Data, Fundamental Data Units
Data Representation
Program Instructions
Languages
C Compilers
Why C is the first language selected?
Some notable features of C
Structure of a simple C Program.